# Text boxes

### ICONSnewspaper26v5_1.icc

The Ifra newspaper printing standardprofile ICONSnewspaper26v5_1.icc is based on the characterisation file “IFRA26.txt” and is valid for the following printing conditions in accordance with the international standard DIS/ISO 12647-3:2004 (status June 2004):

#### Printing conditions

Newspaperoffset 	coldset offset

Standard newsprint 	(45g/m2)

Screen ruling 	40 l/cm ± 2 l/cm (100lpi)

Dot gain 	26%

Measuring background	white

#### Profile production

ProfileMaker 	5.0.5.1.75

Colour space	CMYK

Profile size	standard

Photographic rendering Intend	paper-colour grey

Gamut mapping	LOGO Colorful

ICC profile version	2.4

Produced	21.12.2005

Last edited	21.12.2005

#### Separation settings

Start black	15

max. coverage	240%

max. black	95%

Black dot definition	59-45-41-95

Black width	50

#### Edit

Global correction	chroma 15

For an overview of all all process parameters in accordance with DIS/ISO 12647-3:2004, see www.ifra.com

IfraTraining • 18. – 20. März 2003 • Ifra • Washingtonplatz • Darmstadt